UDEV Rules for USB Hub
- Log into the Tractor
- Connect TTGO Board and GPS to first and second ports on USB hub
- Turn power off to the TTGO Board
Store list of devices connected with power off; $ ls /dev/ > dev_list_1.txt
Turn on power to the TTGO Board
Then run this after you plug it in; $ ls /dev/ | diff --suppress-common-lines -y - dev_list_1.txt / al@al-HP-ProBook-645-G1:~$ ls /dev/ | diff --suppress-common-lines -y - dev_list_1.txt / serial < / ttyACM0 < / al@al-HP-ProBook-645-G1:~$
TTGO Data from: $ dmesg | grep "ttyACM0" / al@al-HP-ProBook-645-G1:~$ dmesg | grep "ttyACM0" / [ 320.747619] cdc_acm 8-1.4:1.0: ttyACM0: USB ACM device / al@al-HP-ProBook-645-G1:~$
$ dmesg | grep "8-1.4" / al@al-HP-ProBook-645-G1:~$ dmesg | grep "8-1.4" / [ 320.527790] usb 8-1.4: new full-speed USB device number 5 using xhci_hcd / [ 320.639556] usb 8-1.4: New USB device found, idVendor=1a86, idProduct=55d4, bcdDevice= 4.43 / [ 320.639574] usb 8-1.4: New USB device strings: Mfr=0, Product=2, SerialNumber=3 / [ 320.639581] usb 8-1.4: Product: USB Single Serial / [ 320.639587] usb 8-1.4: SerialNumber: 5185025965 / [ 320.747619] cdc_acm 8-1.4:1.0: ttyACM0: USB ACM device / al@al-HP-ProBook-645-G1:~$

Get details for GPS
- Run: $ ls /dev/ > dev_list_1.txt
- Turn on power to GPS
al@al-HP-ProBook-645-G1:~$ ls /dev/ > dev_list_2.txt / al@al-HP-ProBook-645-G1:~$ ls /dev/ | diff --suppress-common-lines -y - dev_list_2.txt / gpiochip0 < / ttyUSB0 < / al@al-HP-ProBook-645-G1:~$

- Now “ttyUSB0” appears for GPS
TTGO Data from: $ dmesg | grep "ttyUSB0" / al@al-HP-ProBook-645-G1:~$ dmesg | grep "ttyUSB0" / [ 723.283665] usb 8-1.3: FTDI USB Serial Device converter now attached to ttyUSB0 / al@al-HP-ProBook-645-G1:~$
$ dmesg | grep "8-1.3" / al@al-HP-ProBook-645-G1:~$ dmesg | grep "8-1.3" / [ 723.023008] usb 8-1.3: new full-speed USB device number 6 using xhci_hcd / [ 723.141705] usb 8-1.3: New USB device found, idVendor=0403, idProduct=6001, bcdDevice= 6.00 / [ 723.141719] usb 8-1.3: New USB device strings: Mfr=1, Product=2, SerialNumber=3 / [ 723.141725] usb 8-1.3: Product: FT232R USB UART / [ 723.141730] usb 8-1.3: Manufacturer: FTDI / [ 723.141733] usb 8-1.3: SerialNumber: A907Z09E / [ 723.274412] ftdi_sio 8-1.3:1.0: FTDI USB Serial Device converter detected / [ 723.280071] usb 8-1.3: Detected FT232RL / [ 723.283665] usb 8-1.3: FTDI USB Serial Device converter now attached to ttyUSB0 / al@al-HP-ProBook-645-G1:~$
Create a file /etc/udev/rules.d/05-serial.rules
$ sudo edit /etc/udev/rules.d/05-serial.rules / Copy and paste the lines below / SUBSYSTEM=="tty", ATTRS{idVendor}=="1a86" , ATTRS{idProduct}=="55d4" , ATTRS{serial}=="5185025965", SYMLINK+="ttgo_main" / SUBSYSTEM=="tty", ATTRS{idVendor}=="0403" , ATTRS{idProduct}=="6001" , MODE="0666" , SYMLINK+="gps"

- Ctrl+O; Ctrl+X
- Reboot to apply rules

KERNELS=="8-1.4:1.0", SYMLINK+="ttgo_main" - ttyACM1 (ttgo lora) / KERNELS=="8-1.3:1.0", SYMLINK+="gps" - ttyUSB0 / KERNELS=="8-1.2:1.0", SYMLINK+="odom_left" - ttyACM0 (Teensyduino) / KERNELS=="8-1.1.4:1.0", SYMLINK+="odom_right" - ttyACM2 (Arduino Nano Every) / KERNELS=="8-1.1.3", SYMLINK+="rosimu" - ttyUSB1

Old Notes
Step 7 - Install IMU and visualize the results (2021 version using BNO085/Nano)

Set up udev rule for two Nano’s
- PuTTy into RPi (tractor)
- Store list of devices connected before plugging in the Teensy
- $ ls /dev/ > dev_list_1.txt
- Then run this after you plug it in
- $ ls /dev/ | diff --suppress-common-lines -y - dev_list_1.txt
ubuntu@ubiquityrobot:~$ ls /dev/ | diff --suppress-common-lines -y - dev_list_1.txt / ttyUSB2 < / ubuntu@ubiquityrobot:~$

- $ dmesg | grep "ttyUSB2"
ubuntu@ubiquityrobot:~$ dmesg | grep "ttyUSB2" / [ 2218.636831] usb 1-1.4: ch341-uart converter now attached to ttyUSB2 / ubuntu@ubiquityrobot:~$

$ dmesg | grep "1-1.4"
ubuntu@ubiquityrobot:~$ dmesg | grep "1-1.4" / [ 2217.378209] usb 1-1.4: new full-speed USB device number 11 using dwc_otg / [ 2217.511332] usb 1-1.4: New USB device found, idVendor=1a86, idProduct=7523, bcdDevice= 2.64 / [ 2217.511353] usb 1-1.4: New USB device strings: Mfr=0, Product=2, SerialNumber=0 / [ 2217.511367] usb 1-1.4: Product: USB Serial / [ 2218.634121] ch341 1-1.4:1.0: ch341-uart converter detected / [ 2218.636831] usb 1-1.4: ch341-uart converter now attached to ttyUSB2 / ubuntu@ubiquityrobot:~$
ubuntu@ubiquityrobot:~$ dmesg | grep "1-1.2" / [ 6048.930245] usb 1-1.2: new full-speed USB device number 12 using dwc_otg / [ 6049.073467] usb 1-1.2: New USB device found, idVendor=1a86, idProduct=7523, bcdDevice= 2.64 / [ 6049.073489] usb 1-1.2: New USB device strings: Mfr=0, Product=2, SerialNumber=0 / [ 6049.073503] usb 1-1.2: Product: USB Serial / [ 6049.074713] ch341 1-1.2:1.0: ch341-uart converter detected / [ 6049.077894] usb 1-1.2: ch341-uart converter now attached to ttyUSB2 / ubuntu@ubiquityrobot:~$

- Note there is no serial number for cheap Nano’s. We must use the USB tree to tell them apart. It is important that if I move USB ports this udev rule will have to be updated. Ref, Ref2
- Use FileZilla; Edit /etc/udev/rules.d/05-serial.rules
# the lines below are for two Nano's that have the CH341 chip which does not provide a unique serial number / # this is the best/worst workaround see https://stackoverflow.com/questions/27017203/udev-rule-with-few-parent-device-attributes / # / KERNEL=="ttyUSB[0-9]*", SUBSYSTEM=="tty", ATTRS{idVendor}=="1a86", ATTRS{idProduct}=="7523", ENV{USB_HUB_TYPE}="1a86:7523" / ENV{USB_HUB_TYPE}=="1a86:7523", KERNEL=="ttyUSB[0-9]*",SUBSYSTEM=="tty", KERNELS=="1-1.4:1.0", SYMLINK+="ttyIMUNano" / ENV{USB_HUB_TYPE}=="1a86:7523", KERNEL=="ttyUSB[0-9]*",SUBSYSTEM=="tty", KERNELS=="1-1.2:1.0", SYMLINK+="ttyNano2"

- If interested, $ udevadm info --query=all --name=/dev/ttyUSB2 --attribute-walk
- $ sudo reboot # to check the rules
- $ ls /dev # look for Nano references