Operations – Debugging Tractor Not Starting, No Steering

Ignition switch does not have power
- Check voltage to the red wire on distribution block
- Check the fuse for that slot
- Check the 4 port relay – is the second LED lit; If so, the seat kill switch is active; Is the radio control nearby and working? Is the kill switch enabled?
- Check voltage to the solenoid
- Attach the spare ignition switch
Engine turns over but does not start
- Check kill switch circuits
- Check if the spark plug is getting power

Steering Issues – Things to check
- Power to the steering motor
- Potentiometer plugged in
- Fuse on power distribution block
- On motor controller, do the A and B switches manually move the motor
- Is the radio control sending signals
- Have the PID settings been set